Alex Shah
EN.695.741.81.SP25 Information Assurance Analysis
Mod 4 Assignment
February 18, 2025

1.
For each of the 5 ranges; Connectivity, Link Protocol, Transport,
Session/Communication, and Data Aggregation/Processing, select one (1)
protocol from each which you are unfamiliar with and do the following:
Research the protocol and tell me a bit about it, things like: what frequency band
does it operate at, what transmission rates are supported, what distance is it
suitable for, what devices might it support, and more. Go into a fair bit of detail,
more than what pops up on the first Google search. There should be a total of 5
protocols discussed. 3-4 paragraphs for each protocol is good.

Connectivity: OBD2

An OBD2 connection uses a 16 pin connector most often in automotive applications to read vehicle diagnostics and interact with the onboard computer. Commonly the connector uses the CAN protocol (ISO 15765-4) though there are other ISO and SAE standards used with different pin layouts. The CAN protocol has a baud rate of 250k or 500k to communicate over 2 CAN pins at a peak of 1 Mbps. The protocol is used in emissions testing and engine tuning, and for reading error codes in diagnostics.

OBD2 is usually a wired connection though an adapter like an OBD2 reader can use Bluetooth or Wifi to send data wirelessly over 2.4 Ghz to a device like a phone with an app to read codes and data in real time, or dedicated wired/wireless receivers. This makes OBD2 a short range communication connector, typically within a few feet of the vehicle.

There may be security concerns with an unsecured wireless OBD2 reader attached to a vehicle, allowing private vehicle data to be captured which can be used in a replay attack, or the connection could be used to inject commands to the onboard computer.

Link Protocol: Zigbee

Zigbee operates as a wireless standard, IEEE 802.15.4 to create a PAN (personal area network) as a mesh network where nodes are deployed to pass messages and extend the reach of the network. End devices are usually low powered like IoT devices that communicate over ISM (Industrial, Scientific, Medicine) frequencies like 2.4 Ghz for 250 Kbps data rate or some sub Ghz bands depending on the location, such as 915 Mhz for 40 Kbps in the US. Some of the channels available to Zigbee do not line up with common Wifi 2.4 Ghz channels, ensuring that there are some bands with less interference for Zigbee to conduct its low power transmissions.

The low power <100 mW transmissions travel similar to Wifi distances, up to 100 feet, though some clear line of sight transmission could cover more distance. End devices can hop nodes to reach their destination in the mesh network to cover any distance the mesh can reach. For example lights systems, industrial sensors, or roaming trackers can report status or data to the network. These transmissions can be secured with AES-128 encryption to prevent unauthorized reads when the data hops from node to node. Using Zigbee securely requires a well implemented key management system as well as security patching on the end devices and nodes.

Transport: 6LoWPAN

IPv6 over Low Power Wireless Personal Area Network is another wireless protocol that uses IPv6 packets over a low power wireless network to create a PAN (personal area network) similar to the mesh in Zigbee.

2.
Now that you’re familiar with some of the new IoT-specific protocols, let’s look
at them from a security perspective. From the same diagram, choose one (1)
familiar and one (1) unfamiliar protocol. Detail any ”cyber” attack that is
currently known against each of the protocols. Once complete, compare and
contrast how attacks against IoT protocols are similar to, or different from,
enterprise/legacy IT and OT/ICS network protocols. This should be 3-4
paragraphs for each protocol.

3.

DO node red first flow

4.
Describe how
you would use NODE-Red in an IoT application. You are free to hook it
to ANY device you want to accomplish any task you want. Describe how
you connected NODE-Red to your sensor using API’s and talk about which
NODE-Red components you would use to accomplish it. Explain what you
are trying to solve or accomplish with your IoT application.

Sources

CAN protocols
https://cdn.standards.iteh.ai/samples/67245/caab5ce7ee9b41f8a2f59d60c812c0f7/ISO-15765-4-2016.pdf