Alex Shah
EN.695.741.81.SP25 Information Assurance Analysis
Mod 4 Assignment
February 18, 2025

1.
For each of the 5 ranges; Connectivity, Link Protocol, Transport,
Session/Communication, and Data Aggregation/Processing, select one (1)
protocol from each which you are unfamiliar with and do the following:
Research the protocol and tell me a bit about it, things like: what frequency band
does it operate at, what transmission rates are supported, what distance is it
suitable for, what devices might it support, and more. Go into a fair bit of detail,
more than what pops up on the first Google search. There should be a total of 5
protocols discussed. 3-4 paragraphs for each protocol is good.

Connectivity: OBD2

An OBD2 connection uses a 16 pin connector most often in automotive applications to read vehicle diagnostics and interact with the onboard computer. Commonly the connector uses the CAN protocol (ISO 15765-4) though there are other ISO and SAE standards used with different pin layouts. The CAN protocol has a baud rate of 250k or 500k to communicate over 2 CAN pins at a peak of 1 Mbps. The protocol is used in emissions testing and engine tuning, and for reading error codes in diagnostics.

OBD2 is usually a wired connection though an adapter like an OBD2 reader can use Bluetooth or Wifi to send data wirelessly over 2.4 Ghz to a device like a phone with an app to read codes and data in real time, or dedicated wired/wireless receivers. This makes OBD2 a short range communication connector, typically within a few feet of the vehicle.

There may be security concerns with an unsecured wireless OBD2 reader attached to a vehicle, allowing private vehicle data to be captured which can be used in a replay attack, or the connection could be used to inject commands to the onboard computer.

Link Protocol: Zigbee

Zigbee operates with the wireless standard IEEE 802.15.4 to create a PAN (personal area network) as a mesh network where nodes are deployed to pass messages and extend the reach of the network. Zigbee is a stack from the physical, networking, and application layers as an end to end solution such as for home automation devices like smart devices and sensors. Typically the Zigbee stack isn’t intended to put the devices on the Internet, but allows local communication organized through Zigbee gateway like devices called coordinators.

End devices are usually low powered like IoT devices that communicate over ISM (Industrial, Scientific, Medicine) frequencies like 2.4 Ghz for 250 Kbps data rate or some sub Ghz bands depending on the location, such as 915 Mhz for 40 Kbps in the US. Some of the channels available to Zigbee do not line up with common Wifi 2.4 Ghz channels, ensuring that there are some bands with less interference for Zigbee to conduct its low power transmissions.

The low power <100 mW transmissions travel similar to Wifi distances on 2.4 Ghz, up to 100 feet, though some clear line of sight transmission could cover more distance and sub Ghz could carry signal half a mile. End devices can hop nodes to reach their destination in the mesh network to cover any distance the mesh can reach. For example lights systems, industrial sensors, or roaming trackers can report status or data to the network. These transmissions can be secured with AES-128 encryption to prevent unauthorized reads when the data hops from node to node. Using Zigbee securely requires a well implemented key management system as well as security patching on the end devices and nodes.

Transport: 6LoWPAN

IPv6 over Low Power Wireless Personal Area Network is a link protocol that uses IPv6 packets over a low power wireless network to create a PAN (personal area network). 6LoWPAN, like the Zigbee stack can also use the IEEE 802.15.4 wireless standard, but 6LoWPAN uses standard gateways to adapt IPv6 connectivity for low powered or resource constrained devices. This enables these devices and sensors to connect to the Internet, where the use of IPv6 is intended to help addressing concerns for the large number of devices that are being added to the Internet through IoT.

6LoWPAN can operate through different wireless protocols like IEEE 802.15.4 like Zigbee, or Bluetooth, Wifi, or sub Ghz since it is a protocol on top of an existing physical networking. This means that the distances are similar to Zigbee, where the 2.4 Ghz bands can carry about 100 feet, bluetooth and other protocols could carry signal up to half that distance, or sub Ghz could carry about half a mile. It also supports mesh networking for messages to hop between nodes, and uses strategies like compression and fragmentation to make it more efficient for low power devices to process packets.

Since 6LoWPAN enables Internet connectivity on resource limited devices, processing encryption can be intensive and higher security methods and protocols could be constrained. Typically 6LoWPAN is used on similar devices to Zigbee like environmental monitors, industrial applications, smart agriculture products, and home automation.

Session/Communication: MQTT

Message Querying Telemetry Transport is a publish/subscribe messaging protocol that operates on top of an existing physical/network stack over TCP/IP to coordinate messages between clients via a centralized broker. MQTT is often used on high latency or otherwise unreliable networks to try and send small payloads efficiently. For example MQTT might be deployed in an agriculture setting with a weak existing network for sensors to publish data that a dashboard would subscribe to. The minimal overhead and pub/sub protocol helps ensure that the limited devices and network are still able to relay and receive messages whereas a something like Zigbee experiencing intermittent dropouts could cause lost messages.

Since MQTT can be used on a variety of networks, including Wifi, cellular, and satellite connections. The bands and distances vary with the implementation but the typical size of payloads are bytes to kilobytes in size typically using intermittent or low data rate connections. This low overhead and small payload are useful to ensure message delivery, but create problems for encryption which may increase the resource usage on small low powered devices or create additional overhead.

While MQTT is well suited for small payloads, large feeds like a video or file transmission would be divided into chunks that would increase overhead and add latency. Transport for video would require low latency and is usually done over UDP which does not require confirmation that packets get delivered. So these types of uses go against the benefits that MQTT can provide to the right payloads and would probably overwhelm the network or brokers. An MQTT solution might be to initiate a video feed over a different protocol if a motion sensor is triggered, for example, where the events and metadata are reported over the Message protocol.

Data Aggregation/Processing: Apache Kafka

Kafka is a distributed event streaming platform used for high throughput data applications. Compared to MQTT which has low overhead and can be used on low quality networks, Kafka is meant for continuous large volumes of data to be processed in parallel. It is also a pub/sub model like MQTT but differs in the scale of data being processed at any given time.

While Kafka could be deployed in a limited data situation like MQTT, it would provide the most benefit to cloud environments, or for on site data processing. And unlike MQTT, Kafka uses a distributed log of events enabling persistence of the events and records. While payloads in MQTT might be bytes to kilobytes, Kafka could handle messages several megabytes large. Kafka could work in an agriculture setting with several distributed sensors and process them effectively, but a more realistic use would be lots of messages created continuously like a social media platform where messages are brokered between producers and client feeds.

Kafka can handle slightly larger payloads and more secure methods of encryption since limiting overhead is less of a resource concern on the brokers and higher powered devices that might be generating large amounts of messages. However lower powered devices may not be capable of the high throughput Kafka is intended for. MQTT is still more efficient for small scale deployments and battery powered devices. Millions of messages per second could be passing through Kafka, making it a large scale solution.

2.
Now that you’re familiar with some of the new IoT-specific protocols, let’s look
at them from a security perspective. From the same diagram, choose one (1)
familiar and one (1) unfamiliar protocol. Detail any ”cyber” attack that is
currently known against each of the protocols. Once complete, compare and
contrast how attacks against IoT protocols are similar to, or different from,
enterprise/legacy IT and OT/ICS network protocols. This should be 3-4
paragraphs for each protocol.

Comparing Bluetooth and Zigbee, Bluetooth is in much wider use so threats against Bluetooth devices have a much larger threat target. There are common avenues for Bluetooth attacks like default or easy to guess pairing PINs, and low levels of encryption that can be sniffed and cracked, and since these devices are often used in public, sniffing can be performed passively on a large amount of devices at once.

3.

DO node red first flow

4.
Describe how
you would use NODE-Red in an IoT application. You are free to hook it
to ANY device you want to accomplish any task you want. Describe how
you connected NODE-Red to your sensor using API’s and talk about which
NODE-Red components you would use to accomplish it. Explain what you
are trying to solve or accomplish with your IoT application.

Sources

CAN protocols
https://cdn.standards.iteh.ai/samples/67245/caab5ce7ee9b41f8a2f59d60c812c0f7/ISO-15765-4-2016.pdf